## Slide 1: IP Routing
Ilian Trifonov

## Slide 2: IP Routing
Works based on Routing Tables
Routing tables contain information about what IP address range should be routed to what router next

## Slide 3: Routing Protocols
Classful
  Follows the bit boundaries of Class A, B and C
  Protocols – RIPv1, IGRP
  If we configure 10.20.100.0/24, it would advertise it as a Class A (10.0.0.0/8) because it’s a Class A subnet
Classless
  Follows what is used for the subnet mask to know the network segment
  Protocols – RIPv2, OSPF, EIGRP, IS-IS
  If we configure 10.20.100.0/24, it would advertise it as 10.20.100.0/24, because the subnet mask is indicating what the network is

## Slide 4: Routing Types
Distance Vector – Advertise the full routing table, no network or topology tables
Link State – Maintain neighbor and topology tables, and advertise routing changes only
Hybrid – Combination between Link State and Distance Vector
Path Vector – Used by Border Gateway Protocol (BGP) to determine the best path using one of many attributes

## Slide 5: RIP
Routing Type – Distance Vector
Algorithm – Bellman Ford
Updates – Sends full routing table every 30 seconds
Metric - Hops

## Slide 6: OSPF
Routing Type – Link State
Algorithm – SPF, Dijkstra
Updates – Sends updates when there are changes
Metric – Cost(based on bandwidth)

## Slide 7: EIGRP
Routing Type – Hybrid, Classful/Classless
Algorithm – DUAL
Updates – Sends updates when there are changes
Metric – Composite (Bandwidth, Delay, Load, Reliability etc.)
A routing protocol used by Cisco

## Slide 8: Border Gateway Protocol (BGP)
Routing Type – Path Vector
Algorithm – BGP Best Path Selection Algorithm determines the best route by selecting the shortest path to the destination
Metric – Composite (Weight, Local Preference, AS Path etc.)

## Slide 9: Routing
Router
In
Out
For each packet the router has to decide if it should drop the packet (if there are too many hops for example), or if it should forward, and where it should forward it to.
For that the routers use routing tables and routing protocols

## Slide 10: Routing tables
Addresses on the routing tables are matched by the longest prefix:
124.10.2.0/24
124.10.0.0/16
124.0.0.0/8
If we have to route 124.10.2.122, it will pick 124.10.2.0/24, because it has the longest prefix
This is done because otherwise all routing tables would have to have all 2^32 addresses (over 4 billion)

## Slide 11: Routing
Not all routers on the internet exchange information with each other
Routers are grouped into sub networks and run the routing protocols between the routers on those networks
Routing tables are built by exchange of information between routers in the same sub network
Routing between these sub networks is done with BGP

## Slide 12: Routing

## Slide 13: Link State Routing step 1
Router
Router
Hello packets
Each router talks to the neighboring routers, and builds up information on what it’s connected it

## Slide 14: Link State Routing step 2
The information is sent to all routers on the network so they can build up their neighbor and forwarding tables
Every router knows what every other router is connected to

## Slide 15: Link State Routing step 3
All routers can now run a shortest path algorithm (SPF, Dijkstra etc) to find the optimal way to get the packet to the next network

## Slide 16: Border Gateway Protocol (BGP)
Unlike other protocols, there is only one instance of this protocol running on the internet
Runs between autonomous systems (networks)
ISPs can broadcast the range of IP addresses that are on their networks so they can be reached

## Slide 17: BGP
Problems here have caused widespread issues on the internet
For example when Pakistan tried to stop its citizens from connecting to youtube.com, but instead redirected all the traffic from the entire internet to itself
This happens because of a broadcast of a longer prefix IP address, that gets communicated to all networks around the world. At that point the longest prefix changes, and gets priority
https://www.youtube.com/watch?v=IzLPKuAOe50

## Slide 18: BGP
You can apply routing policies, to give preference to where something should be routed though
Autonomous systems on the internet do not trust each other, and as such they configure many policies on the borders between the autonomous networks, so traffic cannot “leak out” to a network it is not supposed to for example
The most important metric used when deciding where to route with BGP is the autonomous network count to the target IP

## Slide 19: Questions?