## Slide 1: Network Models
TCP/IP and OSI

## Slide 2: Why were these models created
In the 1990s, there were many different networks, standards, computers and operating systems
Arcnet
Linux
Unix
IBM LAN Manager
Appletalk
Localtalk
Novell Networks
Banyan Vines
Ethernet
Token Ring
etc

## Slide 3: There were 4 different types of Ethernet
Apple used Ethernet_SNAP
Novell used Ethernet 802.3
Unix used Ethernet_II
IEEE had IEEE802.3 and 802.2 standards that they were still developing, and the above did not comply with them fully

## Slide 4: The problem
No standard way to communicate between these networks, operating systems and computers
People and companies wanted to share data
Connecting networks of different types often crashed both networks
Companies were running different OS and networks in their different departments, and cannot share data

## Slide 5: ISO OSI Model
International Standards Organization
created the
Open Systems Interconnect model
to solve this interoperability problem

## Slide 6: OSI Model
It is like a unicorn, in that it does not really exist in real life
It is just a model used to describe how networks work
We often use it to describe strict layers in networking, that in practice are not that strictly separated

## Slide 7: TCP/IP model
The actual name is Internet protocol suite
It is the conceptual model and set of communications protocols used on the Internet and similar computer networks. It is commonly known as TCP/IP because the original protocols in the suite are the Transmission Control Protocol (TCP) and the Internet Protocol (IP)
The Internet protocol suite provides end-to-end data communication specifying how data should be packetized, addressed, transmitted, routed and received.
The TCP/IP model, which is realistically the Internet Model, came into existence about 10 years before the OSI model

## Slide 8: TCP/IP model
Originally funded by DARPA (Defense Advanced Research Projects Agency), an agency of the US Department of Defense
Created in the early to mid 1970s
Adoption started in the 1980s
Emphasizes architectural principles over layering
IETF (Internet Engineering Task Force) has stated that Internet protocol and architecture development is not intended to be OSI-compliant. RFC 3439, addressing Internet architecture, contains a section entitled: "Layering Considered Harmful "

## Slide 9: Around the year 2000, the network wars ended
TCP/IP won
TCP/IP is real, and not only conceptual with no implementations
TCP/IP is used by Unix and the internet

## Slide 10: OSI Model
It describes a set of rules of how data is communicated over a network
Also describes network devices down to the hardware

## Slide 11: OSI Model Layers
7. Application Layer
6. Presentation Layer
5. Session Layer
4. Transport Layer
3. Network Layer
2. Data Link Layer
1. Physical Layer
At each layer, two entities at the communicating devices (layer N peers) exchange protocol data units (PDUs) by means of a layer N protocol. Each PDU contains a payload, called the service data unit (SDU), along with protocol-related headers or footers.
Lowest layers are the ones closest to the actual hardware
Highest levels are where communication between application happens

## Slide 12: OSI Model – 7. Application Layer
Consists of network aware applications:
Email
Web Browsers
File sharing services
Print servers
Network drives
Servers (that host sites, services etc)
Etc.

## Slide 13: OSI Model – 6. Presentation Layer
Configures the data:
Encryption
Compression
Translation (Encoding)
This layer provides independence from data representation by translating between application and network formats. The presentation layer transforms data into the form that the application accepts.

## Slide 14: OSI Model – 5. Session Layer
Establishes, manages and terminates the connections between the local and remote application. It is responsible for graceful close of sessions, which is a property of the TCP protocol.

## Slide 15: OSI Model – 4. Transport Layer
Guarantee end to end delivery of data
Check if the destination of the data exists
Get acknowledgement that messages are received
Check if data is not corrupt

## Slide 16: OSI Model – 3. Network Layer
The network layer provides the functional and procedural means of transferring variable length data sequences (called datagrams) from one node to another connected to the same "network“
It has the duty to find the shortest path to the destination

## Slide 17: OSI Model – 2. Data Link Layer
Decides whose turn it is to talk (bus arbitration)
Finds the physical device on the network

## Slide 18: OSI Model – 1. Physical Layer
Describes the physical part of the network
Cables
Voltages
Frequencies
Signal timing
Bits
Transfer rates
The physical layer is never concerned with protocols or other such higher-layer items. Examples of hardware in this layer are network adapters, repeaters, network hubs, modems, and fiber media converters.

## Slide 19: TCP/IP Model vs OSI Model
4 Layers
Application Layer
Transport Layer
Internet Layer
Link Layer
7 Layers
Application Layer
Presentation Layer
Session Layer
Transport Layer
Network Layer
Data Link Layer
Physical Layer

## Slide 20: TCP/IP protocols Application Layer (OSI – Application, Presentation, Session)
HTTP - Hypertext Transfer Protocol
HTTPS
FTP
IRC – Chat protocol
SNMP – Network management protocol
POP3 – Mail protocol
SMTP – Mail protocol
DNS – Domain name to IP
Telnet - bidirectional interactive text-oriented communication facility using a virtual terminal connection.
SSH – Like Telnet, but with encryption
TFTP – File transfer protocol
NTP – Clock synchronization protocol

## Slide 21: TCP/IP protocols Transport Layer (OSI – Transport)
TCP (Transmission Control Protocol)
  Guarantees end to end delivery of data
  Connection based
UDP (User Datagram Protocol)
  Does not guarantee end to end delivery of data
  Send and Pray
  Connectionless

## Slide 22: TCP/IP protocols Internet Layer (OSI – Network)
IP (Internet Protocol) – used relaying datagrams across network boundaries, Its routing function enables internetworking, and essentially establishes the Internet.
ICMP (Internet Control Message Protocol) - used by network devices, including routers, to send error messages and operational information
IGMP (Internet Group Management Protocol) – used to establish multicast group memberships for IPv4

## Slide 23: TCP/IP protocols Link Layer (OSI – Data Link, Physical)
Ethernet
IEEE 802
ARP (Address Resolution Protocol) - communications protocol used for resolution of Internet layer addresses into link layer addresses
RARP (Reverse Address Resolution Protocol)
NDP (Neighbor Discovery Protocol) – Similar to ARP by for IPv6

## Slide 24: Protocol Data Units (PDUs)
Generic term used to describe a layer’s information
Each TCP/IP layer has a PDU associated with it

## Slide 25: 4. Application Layer PDU
DATA
The data can be:
Clear text
Encrypted
Compressed

## Slide 26: 3. Transport Layer PDU
For TCP – segment
For UDP – datagram
Generally we have a header, footer and the segment or datagram

## Slide 27: 2. Internet Layer PDU
Packet

## Slide 28: 1. Link Layer PDU
Here it is easier to talk in terms of the OSI model:
Data Link layer – frames (Ethernet frames)
Physical layer – bits

## Slide 29: PDU Summary
Application Layer – Data
Transport Layer – Segments or Datagrams
Internet Layer – Packets
Link Layer – Frames and Bits

## Slide 30: Layer Addressing
Each layer has an addressing scheme to identify services
Source and destination address

## Slide 31: Application/Transport Layer Addressing
Ports - a numbered logical construct allocated specifically for each of the communication channels an application needs
For many types of services, these port numbers have been standardized so that client computers may address specific services of a server computer without the involvement of service announcements or directory services.
HTTP – 80
HTTPS – 443
Telnet – 23
FTP – 20 and 21
DNS – 53
Clients are dynamically assigned ports from 8000 to 65535

## Slide 32: Internet Layer Addressing
Uses IP Addresses
IPv4 uses 32 bit addresses to identify hosts
IPv6 uses 128 bit addresses to identify hosts
Looks like 192.168.100.254 (IPv4)

## Slide 33: Link Layer Addressing
Physical address, also called MAC address (media access control)
It is a unique identifier assigned to network interfaces for communications at the data link layer of a network segment. MAC addresses are used as a network address for most IEEE 802 network technologies, including Ethernet and Wi-Fi.
48 bit hexadecimal number
Looks like 00.12.f4.B.0C.82 (can be separated by dots, dashes etc or not at all)

## Slide 34: Addressing Summary
Application Layer – No addressing
Transport Layer – Ports
Internet Layer – IP Addresses
Network Layer – Physical Addresses

## Slide 35: Devices on the different layers
We can map network devices to the TCP/IP and OSI models

## Slide 36: Physical Layer (OSI model)
Works on bits
Repeaters – extend the LAN, and now commonly called transceivers
Multiport Repeaters – HUB - Obsolete

## Slide 37: Data Link Layer (OSI model)
Works on frames, and the addressing is the MAC address
The devices make decisions based on the physical address to forward or not to forward frames (to reduce congestion or break up the network into smaller parts, or do security)
Devices are Bridges that examine frames
Multiport Bridges called Switches

## Slide 38: Internet/Network Layer Devices
Works on packets, addressing is done with IP addresses
Devices examine the packets and make decisions based on the IP address to forward or not to forward the packet
Devices here are Routers and Layer 3 Switches (that do the job of a router and a switch)

## Slide 39: Transport Layer Devices
Work on segments, and the addressing is ports
Devices examine the segments and make decision based on the port, to forward or not to forward the segment
Firewalls make decisions based on the port number

## Slide 40: Application Layer Devices
Works on data, and there is no addressing
Devices examine the contents of the data and make decisions based on the contents to forward or not to forward the data
ALG (Application Layer Gateway) make decisions based on the content of the data

## Slide 41: Device Summary
Application Layer – ALG (Application Layer Gateway) – Data
Transport Layer – Firewalls – Ports
Internet/Network Layer – Routers and Layer 3 Switches – IP Addresses
Data Link Layer – Bridges and Switches – Physical Addresses
Physical Layer – Repeaters (transceivers) and Hubs - Bits

## Slide 42: TCP/IP Model vs OSI Model Summary
4 Layers
Application Layer
Transport Layer
Internet Layer
Link Layer
7 Layers
Application Layer
Presentation Layer
Session Layer
Transport Layer
Network Layer
Data Link Layer
Physical Layer

## Slide 43: PDU Summary
Application Layer – Data
Transport Layer – Segments or Datagrams
Internet Layer – Packets
Link Layer – Frames and Bits

## Slide 44: Addressing Summary
Application Layer – No addressing
Transport Layer – Ports (http:80, https:443, Telnet: 23)
Internet Layer – IP Addresses (192.168.100.254)
Network Layer – Physical Addresses (00.12.F4.AB.0C.82)

## Slide 45: Device Summary
Application Layer – ALG (Application Layer Gateway) – Data
Transport Layer – Firewalls – Ports
Internet/Network Layer – Routers and Layer 3 Switches – IP Addresses
Data Link Layer – Bridges and Switches – Physical Addresses
Physical Layer – Repeaters (transceivers) and Hubs - Bits